## Slide 1
Voxel Dance Software Integration

## Slide 2: Installation of VD
Another step to ensure a proper installation and activation of the software is to run the installer as an administrator. To do this, simply right-click on the installer and select "Run as administrator." Additionally, make sure that your firewall or antivirus software is not blocking the server connection required for activation. If necessary, you may need to temporarily disable your antivirus software during this process. Please note that this step only needs to be done once.

## Slide 3
Adding machine profiles
Go to create the platform, machine definition, and choose the desirable photocentric printer and press create the platform now your printer is added to the library, and you can create the platform.

## Slide 4
Import machine profiles
Go to create the platform, machine definition, right click on My Machine section, Import, and choose .vdafpg format machine profile.

## Slide 5: Importing Photocentric Support Profiles
Open VD software, go to support module, choose which profiles you want to export/import in the settings options. Supports profiles can be found in the photocentric installer pack under the folder name supports profiles

## Slide 6
Importing Photocentric Supports Profiles
You can export also all settings you change/modify including UI settings colours etc. something similar to Studio. It's called Global Parameters, go to the file, options and tab Import/Export

## Slide 7
Slicing
Before Slice the file in VD, make sure to apply Shrinkage Correction by scaling part only XY direction by +1% (Highlight all parts>>>Scale>>>Set XY parameters to 101.000%>>>Apply>>>Refresh Supports) (Image 1)
Click Slice. When you are creating VD new Titan machine profile just copy the build platform parameters from the studio, and then when you will slice the file in VD just make sure you have a correct resolution of 7680x4320 of the screen and that the pixel size is 90.9 microns, you can copy this from the studio as well. (See image 2) (Once these parameters are set it stays as default)
2
1

## Slide 8
Converter
Print file – Choose Sliced zip file
Output – place where crs for Titan will appear
Choose printer
Resin Profile (100um/250um works for both Hard Black and DL110HB)